## Slide 1: Unsupervised Batch Clustering of Neural Spikes
Scott Grimes - HIWI

## Slide 2: Manual Spike Sorting is Tedious
Adapted from Quian Quiroga et al. (2004)
General Sorting Steps:
i) The raw data is filtered
ii) Spikes are extracted from the data using an amplitude threshold
iii) Spikes features are determined (giving a dimensionality reduction)
iv) Spikes are clustered

## Slide 3: Automated Procedure
Spikes are extracted from filtered data using amplitude detection (positive, negative, or both) in standard deviations

## Slide 4: Automated Procedure
Spikes are aligned to each other using their extreme amplitudes for sorting. There are two primary clustering methods available: Principal Component Analysis and Superparamagetic Clustering. Artifacts may be removed at this point using an amplitude threshold if they were not already removed during the initial importation.
Pre-Clustered Post-Clustered

## Slide 5: Superparamagnetic Clustering
For sorting the Principal Component Loadings without knowing the final number of clusters initially we can work backwards, over-clustering and then merging similar clusters until convergence
As T increases, the number of clusters increases and the size of the clusters decreases. The cost function which determines which spikes to include in a given cluster is fixed, which can leave many spikes un-clustered or ill-clustered.
Superparamagnetic clustering of data--The definitive solution of an ill-posed problem
E Domany - Physica A: Statistical Mechanics and its Applications, 1999 - Elsevier
Low T
Not Clustered
High T
Over-Clustered

## Slide 6: Principal Component Analysis for N-Unknown Clusters
Example Adapted from MATLAB User Guide
The loadings for n spikes are computed. In this example The vector latent is the eigenvalues of the covariance matrix of ingredients
Here the first two components account for ~98% of the variance in the set. We can reduce each spike vector to loadings with a small dimension which reduces the computation time required for clustering.

## Slide 7: Principal Component Analysis for N-Unknown Clusters
Once the number of required components are know we can begin clustering.
K-means clustering attempts to minimize the sum of squares within each cluster for an initial cluster guess M.
However we do not know the final number of clusters, so k-means is initialized with an arbitrary value M, known to be greater than N, the final number of clusters.
kmeans infographic

## Slide 8: Principal Component Analysis for N-Unknown Clusters
A similarity matrix is computed for M clusters where Mij is the similarity of the clusters i and j.
For M-1 iterations the clusters with the greatest similarity are combined, and a new similarity matrix is computed…
In this example cluster 14 is merged into cluster 4

## Slide 9: Principal Component Analysis for N-Unknown Clusters
When the number of clusters has been reduced from M to 2, the maximum similarity between clusters for every iteration of M is taken:
The maximum cluster similarity in iteration 3 was far greater than previous iterations, all similar clusters have been collected together at this point. We can use the cluster indexes of this iteration (3 final number of clusters).

## Slide 10: Post-Processing Review
Several tools are included to review the clusters after they have been sorted:
Clusters can be combined or discarded. Spikes shapes and ISI histograms can be plotted. Clusters may be overlaid for comparison.

## Slide 11: Post-Processing Review
Timelines for each cluster can be created using the spike shapes and timestamps for each event (plotted together or separately for comparison)

## Slide 12: Post-Processing Review
The inter-spike interval histogram and average rate of fire for each cluster is shown on the left.
Cluster shapes with standard deviation shown on the right

## Slide 13: Interface